## Slide 1
IEEE 802.11 WLAN

## Slide 2: History
FCC decided to authorize public use of ISM band in
mid-80s
  No need to obtain FCC licenses
This resulted in substantial growth of WLAN products
Due to lack of standards proprietary products appeared
  Divided the market
  Parts were incompatible
Working group IEEE 802.11 was established
  Defined physical and MAC sub-layer standards in
June 1997

## Slide 3
802.11 Family
Another standard HIPERLAN was developed in Europe
It offered rates between 2 and 25Mbps in 5.2 GHz
 | 802.11 | 802.11a | 802.11b | 802.11g | 802.11n
Freq. Band | 2.4GHz | 5 GHz | 2.4 GHz | 2.4 GHz | 2.4GHz
Max. data rate | 2Mbps | 54Mbps | 11Mbps | 54 Mbps | 248Mbps

## Slide 4
Benefits of Wireless LANs
Some jobs require people to physically move while using an appliance, which exchanges information with another appliance or central computer
  Wired LANs poses difficulty in implementation
  WLAN is technology of choice
Reduction in infrastructure and operating cost
Useful where wiring is not possible
Fast deployment
No cable faults: reduced downtime

## Slide 5
WLAN applications
LAN Extension
  WLAN cannot substitute existing wired network
  Suitable for flexible extension of wired networks
Cross-building interconnection
  Connecting wired LANs located in nearby buildings
  Point-to-point link controlled by a device that incorporates a router functionality

## Slide 6
WLAN applications
Nomadic access
  Employee transferring data on return from a tour,
from his laptop to the server
  Students accessing information offered by university server from anywhere in the campus
Ad hoc networking
  A peer-to-peer network, setup to satisfy a temporary need
  Conference room or business meetings where participants use portable computers to form a network in order to share information

## Slide 7
802.11 Network Architecture
802.11 defines a hierarchical Network architecture
  Allows WLAN equipment to be configured in a
variety of ways
  End-points are called stations, have a NIC
  Simplest configuration is called as BSS
    Supports direct communication between
members
  Using BSS, we can build
    Independent BSS, Infrastructure BSS, Extended service set

## Slide 8
WLAN Components
Wireless LAN Station
  The station (STA) is the most basic component of the
wireless network.
  A station is any device that contains the functionality of the
802.11 protocol, that being MAC, PHY, and a connection to the wireless media.
Typically the 802.11 functions are implemented in the
hardware and software of a network interface card (NIC)
A station could be a laptop PC, handheld device, or an Access Point.
Stations may be mobile, portable, or stationary
Basic Service Set (BSS)
  basic building block of an 802.11 wireless LAN.
  The BSS consists of a group of any number of stations.

## Slide 9
Independent Basic Service Set

## Slide 10: IBSS
A set of stations, which have recognized each other and are connected via the wireless media in a peer- to-peer fashion.
Also called an Ad-hoc network.
The mobile stations communicate directly with each
other.
There are no relay functions in an IBSS therefore all stations need to be within range of each other and communicate directly.
Effective for a temporary need
No provision to access wired network

## Slide 11
Infrastructure BSS
Backbone

## Slide 12
Infrastructure BSS
BSS with a component called an Access Point (AP).
The access point provides a local relay function for
the BSS.
All stations in the BSS communicate with the access point and do not communicate directly.
All frames are relayed between stations by the
access point.
This local relay function effectively doubles the range of the IBSS.
The access point may also provide connection to a
distribution system.

## Slide 13
Extended Service Set

## Slide 14
ESS
Extends the range of mobility to an arbitrary range
Set of infrastructure BSS’s, where the access points communicate amongst themselves to forward traffic from one BSS to another
The access point performs this communication through the distribution system, which may be constructed of either a wired LAN or wireless network.
The distribution system is a thin layer in each access point that
determines the destination for traffic received from a BSS.
  relayed back to a destination in the same BSS
  forwarded on the distribution system to another access point
  sent into the wired network to a destination not in the extended service set.

## Slide 15
ESS
Communications received by an access point from the distribution system are transmitted to the BSS to be received by the destination mobile station.
Network equipment outside of the extended service set views the ESS and all of its mobile stations as a single MAC-layer network where all stations are physically stationary.
ESS hides the mobility of the mobile stations from everything outside the ESS.
This level of indirection provided by the 802.11 architecture allows existing network protocols that have no concept of mobility to operate correctly with a wireless LAN where there is mobility.

## Slide 16: Network Services
Distribution
  Used by mobile stations in Infrastructure BSS,
every time they send data.
  Once a frame has been access by access point, it uses distribution service to deliver the frame
    This is true even for two mobile stations
associated with same access point
Integration
  Service provided by the distribution system
  It allows connection of the distribution system to the non-IEEE 802.11 network

## Slide 17: Network Services
58
Association
  Request from client and response from AP.
  Finalizes security options
  Finalizes bit rate options
  Sets up data link
  Client learns the access point MAC address (BSSID)
  Delivery of frames to mobile stations is possible because they register or associate with access point
  The distribution system uses the registration information to determine which access point to use for a mobile station
– Unassociated stations are not “on the network”

## Slide 18: Network Services
Reassociation
  When a mobile station moves between BSS areas, within a single ESS, it evaluates signal strength and may switch the access point with which it is associated.
  Reassociations are initiated by STA, when signal conditions indicate that a association with a different AP is beneficial
  After Reassociation is complete, distribution system
updates it location records

## Slide 19: Network Services
Disassociation
  Used for terminating an existing association
  Mobility data stored in the distribution system is revoked
  A polite task to do during STA shutdown
  MAC is designed to handle STA that leave network
without disassociating

## Slide 20: Network Services
Authentication
  Wireless networks cannot offer same level of
physical security as wired LAN
    Network attachment points in wired LAN can be secured in locked closets
  Additional authentication routines are required to
ensure only authorised users are allowed
  In practice, many access points are configured for “open system” authentication

## Slide 21: Network Services
Privacy
  Eavesdropping on wireless network can be comparatively simpler by using correct antenna and modulation methods
  Optional privacy service Wired Equivalent Privacy
(WEP) is available.
    Uses encryption techniques
    WEP is not iron clad securtiy

## Slide 22
802.11b Security Features
Wired Equivalent Privacy (WEP) – A protocol to protect link-level data during wireless transmission between clients and access points.
Services:
  Authentication: provides access control to the network by denying access to client stations that fail to authenticate properly.
  Confidentiality: intends to prevent information compromise from casual eavesdropping
  Integrity: prevents messages from being modified while in transit between the wireless client and the access point.

## Slide 23
Authentication
Authentication techniques

## Slide 24: Privacy
Cryptographic techniques
WEP Uses RC4 symmetric key, stream cipher algorithm to generate a pseudo random data sequence. The stream is XORed with the data to be transmitted
Key sizes: 40bits to 128bits
Unfortunately, recent attacks have shown that the WEP approach for privacy is vulnerable to certain attack regardless of key size

## Slide 25
Data Integrity
Data integrity is ensured by a simple encrypted
version of CRC (Cyclic Redundant Check)
Also vulnerable to some attacks

## Slide 26
Security Problems
Security features in Wireless products are frequently
not enabled.
Use of static WEP keys (keys are in use for a very long time). WEP does not provide key management.
Cryptographic keys are short.
No user authentication occurs – only devices are authenticated. A stolen device can access the network.
Identity based systems are vulnerable.
Packet integrity is poor.

## Slide 27: Mobility Support
BSS transition
  Stations continuously monitor the signal strength
from all APs in a ESS area
  Within an ESS, 802.11 provides MAC layer mobility
  STAs use reassociation service to associate with a
new AP
  New access point needs to inform old access point about the association
    Not standardized as a protocol

## Slide 28: Mobility Support
ESS transition
  802.11 does not support this type of transitions
    It allows STA to associate with an AP in new ESS
  Higher layer connections are guaranteed to be distributed
  Maintaining high level connection requires support
from protocol
    In case of TCP/IP, mobile IP is required to seamlessly support ESS transitions

## Slide 29
Part of the 802.11 Protocol Stack

## Slide 30
Protocol Stack across Network

## Slide 31
Thank You
491