## Slide 1: NETWORK TOPOLOGY

## Slide 2: Topology
It is the shape or physical connectivity of the network.
Goals when establishing topology
  Provide maximum possible reliability to assure proper receipt of all traffic
  Route the traffic across the least cost path within the network.
  Give the end user the best possible response time and throughput
Each topology has advantages & disadvantages

## Slide 3: Types of Topologies
Star
  Easy to install
  Central element, a hub or a switch
  Localisation of problem
  Hub is the weakest element
Bus
  Easy to expand, shorter cables
  Single conversation, all station can hear every transmission
  Bus is the weakest element

## Slide 4: Types of Topologies
Ring
  Deterministic
  Dual path, redundant
  Poor scalability
Line
  Open ring
Tree
  Mesh network with no redundancy
  Provides a concentration point for control and error resolution and potential bottleneck

## Slide 5: Types of Topologies
Mesh
  Multiple paths are available
  Reconfiguration possible
  Multiple hops
  Wiring complicated
Fully connected network
  Extended mesh network
  Fast, no hops
  Poor scalability