## Slide 1: ZigBee/IEEE 802.15.4 Overview

## Slide 2: New trend of wireless technology
Most Wireless industry focuses on increasing high data throughput
A set of applications require simple wireless connectivity, relaxed throughput, very low power, short distance and inexpensive hardware.
  Industrial
  Agricultural
  Vehicular
  Residential
  Medical

## Slide 3: What is ZigBee Alliance?
An organization with a mission to define reliable, cost effective, low-power, wirelessly networked, monitoring and control products based on an open global standard
Alliance provides interoperability, certification testing, and branding

## Slide 4: IEEE 802.15 working group

## Slide 5: Comparison between WPAN

## Slide 6: ZigBee/IEEE 802.15.4 market feature
Low power consumption
Low cost
Low offered message throughput
Supports large network orders (<= 65k nodes)
Low to no QoS guarantees
Flexible protocol design suitable for many applications

## Slide 7: ZigBee network applications
PERSONAL HEALTH CARE
ZigBee
LOW DATA-RATE
RADIO DEVICES
HOME AUTOMATION
CONSUMER ELECTRONICS
TV VCR
DVD/CD
Remote control
security
HVAC
lighting
closures
PC & PERIPHERALS
consoles portables
educational
TOYS &
GAMES
INDUSTRIAL & COMMERCIAL
monitors
sensors
automation
control
mouse
keyboard
joystick
monitors
diagnostics
sensors

## Slide 8: Wireless technologies
10
100
1,000
10,000
10
100
1,000
10,000
100,000
Bandwidth
kbps
GSM
802.11a/g
GPRS
EDGE
2000
2003-4
2005
Bluetooth
3G
Hiper
LAN/2
Bluetooth 2.0
Range
Meters
802.11b
ZigBee
WiMedia
Bluetooth 1.5

## Slide 9: ZigBee/802.15.4 architecture
ZigBee Alliance
  45+ companies: semiconductor mfrs, IP providers, OEMs, etc.
  Defining upper layers of protocol stack: from network to application, including application profiles
  First profiles published mid 2003
IEEE 802.15.4 Working Group
  Defining lower layers of protocol stack: MAC and PHY

## Slide 10: How is ZigBee related to IEEE 802.15.4?
ZigBee takes full advantage of a powerful physical radio specified by IEEE 802.15.4
ZigBee adds logical network, security and application software
ZigBee continues to work closely with the IEEE to ensure an integrated and complete solution for the market

## Slide 11: IEEE 802.15.4 overview

## Slide 12: General characteristics
Data rates of 250 kbps , 20 kbps and 40kpbs.
Star or Peer-to-Peer operation.
Support for low latency devices.
CSMA-CA channel access.
Dynamic device addressing.
Fully handshaked protocol for transfer reliability.
Low power consumption.
Channels:
  16 channels in the 2.4GHz ISM band,
  10 channels in the 915MHz ISM band
  1 channel in the European 868MHz band.
Extremely low duty-cycle (<0.1%)

## Slide 13: IEEE 802.15.4 basics
802.15.4 is a simple packet data protocol for lightweight wireless networks
  Channel Access is via Carrier Sense Multiple Access with collision avoidance and optional time slotting
  Message acknowledgement
  Optional beacon structure
  Target applications
    Long battery life, selectable latency for controllers, sensors, remote monitoring and portable electronics
  Configured for maximum battery life, has the potential to last as long as the shelf life of most batteries

## Slide 14: IEEE 802.15.4 Device Types
There are two different device types :
  A full function device (FFD)
  A reduced function device (RFD)
The FFD can operate in three modes by serving as
  Device
  Coordinator
  PAN coordinator
The RFD can only serve as:
  Device

## Slide 15: FFD vs RFD
Full function device (FFD)
  Any topology
  Network coordinator capable
  Talks to any other device
Reduced function device (RFD)
  Limited to star topology
  Cannot become a network coordinator
  Talks only to a network coordinator
  Very simple implementation

## Slide 16: Star topology
Full Function Device (FFD)
Reduced Function Device (RFD)
Communications Flow
Network
coordinator
Master/slave
Network
coordinator

## Slide 17: Peer to peer topology
Communications Flow
Full Function Device (FFD)
Point to point
Tree

## Slide 18: Device addressing
Two or more devices communicating on the same physical channel constitute a WPAN.
  A WPAN includes at least one FFD (PAN coordinator)
  Each independent PAN will select a unique PAN identifier
Each device operating on a network has a unique 64-bit extended address. This address can be used for direct communication in the PAN
A device also has a 16-bit short address, which is allocated by the PAN coordinator when the device associates with its coordinator.

## Slide 19: IEEE 802.15.4 physical layer

## Slide 20: IEEE 802.15.4 PHY overview
PHY functionalities:
  Activation and deactivation of the radio transceiver
  Energy detection within the current channel
  Link quality indication for received packets
  Clear channel assessment for CSMA-CA
  Channel frequency selection
  Data transmission and reception

## Slide 21: IEEE 802.15.4 PHY Overview
868MHz/
915MHz
PHY
2.4 GHz
868.3 MHz
Channel 0
Channels 1-10
Channels 11-26
2.4835 GHz
928 MHz
902 MHz
5 MHz
2 MHz
2.4 GHz
PHY
Operating frequency bands

## Slide 22: Frequency Bands and Data Rates
The standard specifies two PHYs :
  868 MHz/915 MHz direct sequence spread spectrum (DSSS) PHY (11 channels)
    1 channel (20Kb/s) in European 868MHz band
    10 channels (40Kb/s) in 915 (902-928)MHz ISM band
  2450 MHz direct sequence spread spectrum (DSSS) PHY (16 channels)
    16 channels (250Kb/s) in 2.4GHz band

## Slide 23: PHY Frame Structure
Preamble
Start of
Packet
Delimiter
PHY Header
PHY Service
Data Unit (PSDU)
4 Octets
0-127 Bytes
Sync Header
PHY Payload
1 Octets
1 Octets
Frame
Length
(7 bit)
Reserve
(1 bit)
PHY packet fields
  Preamble (32 bits) – synchronization
  Start of packet delimiter (8 bits) – shall be formatted as “11100101”
  PHY header (8 bits) –PSDU length
  PSDU (0 to 127 bytes) – data field

## Slide 24: IEEE 802.15.4 MAC

## Slide 25: Superframe
A superframe is divided into two parts
  Inactive: all station sleep
  Active:
    Active period will be divided into 16 slots
    16 slots can further divided into two parts
        Contention access period
        Contention free period

## Slide 26: Superframe
Beacons are used for
  starting superframes
  synchronizing with other devices
  announcing the existence of a PAN
  informing pending data in coordinators
In a “beacon-enabled” network,
  Devices use the slotted CAMA/CA mechanism to contend for the usage of channels
  FFDs which require fixed rates of transmissions can ask for guarantee time slots (GTS) from the coordinator

## Slide 27: ZigBee Network Layer Protocols

## Slide 28: ZigBee Network Layer Overview
Three kinds of networks are supported: star, tree, and mesh networks

## Slide 29: ZigBee Network Layer Overview
Three kinds of devices in the network layer
  ZigBee coordinator: responsible for initializing, maintaining, and controlling the network
  ZigBee router: form the network backbone
  ZigBee end device: must be connected to router/coordinator
In a tree network, the coordinator and routers can announce beacons.
In a mesh network, there is no regular beacon.
  Devices in a mesh network can only communicate with each other in a peer-to-peer manner

## Slide 30: Address Assignment
In ZigBee, network addresses are assigned to devices by a distributed address assignment scheme
ZigBee coordinator determines three network parameters
  the maximum number of children of a ZigBee router
  the maximum number of child routers of a parent node
  the depth of the network

## Slide 31
C

## Slide 32: ZigBee Routing Protocols
In a tree network
  Utilize the address assignment to obtain the routing paths
In a mesh network:
    Routing Capability: ZigBee coordinators and routers are said to have routing capacity if they have routing table capacities and route discovery table capacities
    There are 2 options:
      Reactive routing: if having “routing capacity”
      Tree routing: if having no routing capacity

## Slide 33: ZigBee Tree Routing
When a device receives a packet, it first checks if it is the destination or one of its child end devices is the destination
  If so, accept the packet or forward it to a child
  Otherwise, relay it along the tree
Example:
  38  45
  38  92

## Slide 34: ZigBee Mesh Routing
Route discovery by using routing protocol
  The cost of a link is defined based on the packet delivery probability on that link
Route discovery procedure
  The source broadcasts a route request packet
  Intermediate nodes will rebroadcast route request if
    They have routing discovery table capacities
    The cost is lower
  Otherwise, nodes will relay the request along the tree
  The destination will choose the routing path with the lowest cost and then send a route reply

## Slide 35: Routing in a Mesh network: Example

## Slide 36: Summary of ZigBee network layer
 | Pros | Cons
Star | 1. Easy to synchronize 2. Support low power operation 3. Low latency | 1. Small scale
Tree | 1. Low routing cost 2. Can form superframes to support sleep mode 3. Allow multihop communication | 1. Route reconstruction is costly 2. Latency may be quite long
Mesh | 1. Robust multihop communication 2. Network is more flexible 3. Lower latency | 1. Cannot form superframes (and thus cannot support sleep mode) 2. Route discovery is costly 3. Needs storage for routing table