## Slide 1
The Cellular Concept
© 2011, HTDG,C-DAC

## Slide 2: Mobile phone Generations

## Slide 3
History of cellular Systems
© 2011, HTDG,C-DAC
Initial mobile networks were called 1G and were
based on analog communication in radio paths.
The early 1990 saw replacement of 1G networks with 2G which used digital communication in radio paths.
Four competing technologies were deployed:
  GSM
  IS-95
  PDC
  US-TDMA(or D-AMPS)

## Slide 4
2G Systems
© 2011, HTDG,C-DAC
GSM: European Telecom Standards Institute
developed the GSM specifications in 1989.
– It used 25Mhz spectrum in 900MHz band. Later 1800MHz and 1900Mhz bands were added
IS-95: Based on CDMA scheme developed by
Qualcomm.
PDC: Personal Digital Cellular was popular in Japan
US-TDMA was popular in US, called as D-AMPS and was backward compatible with 1G system AMPS

## Slide 5
Evolution of Cellular Networks
1G
2G
3G
4G
2.5G

## Slide 6
GSM
© 2011, HTDG,C-DAC

## Slide 7
What is GSM?
© 2011, HTDG,C-DAC
Global System for Mobile communication (derived from original Groupe Spécial Mobile)
– In 1982, CEPT created the GSM to develop a standard for a mobile telephone system that could be used across Europe
Original GSM (or GSM900) is now supplemented by
GSM1800(or DCS1800) and GSM1900 (or PCS1900)
More than 70% of mobile users in the world use GSM technology
GSM technology covers more than 80% population of
the world

## Slide 8
Structure of GSM Network
© 2011, HTDG,C-DAC
Functional entities of GSM
  The Mobile Station(MS)
    Also called as handset
    Provides access to the user
  The Base Station Subsystem (BSS)
    Base stations and their controllers
  The Network Switching Subsystem (NSS)
    The part most similar to a fixed network
    This is sometimes also just called the core network
    Used for connecting calls among users

## Slide 9
Structure of GSM Network
© 2011, HTDG,C-DAC
Functional entities of GSM (continued)
  The Operation Support Subsystem(OSS)
    For configuring the network
    For maintenance of the network
  The GPRS Core Network
    optional part which allows packet based Internet
connections
Functions and interfaces are defined are defined in the standard

## Slide 10
PLMN: The area covered by one network operator. A PLMN can contain one or more MSCs
© 2011, HTDG,C-DAC

## Slide 11
BSC
BTS
BTS
Mobile Station
Access Network:
Base Station Subsystem
HLR
VLR EIR
AuC
MSC
PSTN
Um
Abis
A
Core Network: GSM CS network
SS7
© 2011, HTDG,C-DAC
GSM Network Architecture

## Slide 12
Key Elements in GSM Network
© 2011, HTDG,C-DAC

## Slide 13
GSM Interfaces
© 2011, HTDG,C-DAC
Um Interface
  Mobile Station and Base Station Subsystem communicate across Um interface, also known as air interface or radio link.
Abis interface
  Base Transceiver Station (BTS) and Base Station Controller (BSC) communicate across Abis interface.
A interface
  Base Station Subsystem communicates with Mobile service Switching Center (MSC) across A interface.

## Slide 14
GSM Functional Entities(contd.)
© 2011, HTDG,C-DAC
Registers
  HLR – Home Location Register
  VLR – Visitor Location Register
  AUC – Authentication Centre
  EIR – Equipment Identification Register

## Slide 15
Subscriber Identity Module
A small smart card
Encryption codes needed to identify the subscriber
Subscriber IMSI(International mobile subscriber identity) number
Subscriber’s own information (telephone directory)
Third party applications (banking etc.)
Can also be used in other systems besides GSM, e.g., some WLAN access points accept SIM based user authentication

## Slide 16
Subscriber Identity Module (SIM)
© 2011, HTDG,C-DAC
The smart card provided by service provider
Plugs into Mobile Equipment and remains in it, till
duration of use
Stores the 15 digit International Mobile Subscriber Identity (IMSI)
  The first 3 digits are the Mobile Country Code
  Next 3 digits are Mobile Network Code
  The remaining digits are the mobile station identification number (MSIN) within the network's customer base

## Slide 17
Subscriber Identity Module (SIM)
© 2011, HTDG,C-DAC
SIM carries following information
  IMSI
  Authentication Key
  Subscriber Information
  Access control class
  Forbidden PLMN (Public Land Mobile Network)
  Cipher key
  TMSI(Temporary Mobile Subscriber Identity )
  Additional GSM services
  Location Area Identity

## Slide 18
1G Cellular Systems
Analog signaling for user traffic
No encryption
  eavesdropping possible
Inferior call quality
  Easily degraded by noise
Spectrum inefficiency
  Each RF carrier is dedicated to single user regardless of whether the user is active (speaking) or not (idle within the call)
AMPS(Advanced Mobile Phone System) in US
TACS(Total Access Communication System) in Europe

## Slide 19: Advanced Mobile Phone System
Developed by Bell labs and deployed in 1982
Uses a number of 30Khz channels
Carries only voice.
AMPS was allocated bandwidth in 800MHz by FCC
Each cellular telephone includes a Numeric Assignment Module (NAM) in ROM
  Telephone number
  Serial number of the unit
  When phone is turned on this info. is sent to MTSO

## Slide 20
2G Cellular Systems
353
Key improvements over 1G
  Digital traffic channels
    Readily support digital data
    Voice is encoded in digital form
  Encryption
    Encryption of all traffic to prevent eavesdropping
  Error detection and correction
    Results in better voice reception
  Channel access
    Each channel is dynamically shared between
users

## Slide 21
2G Cellular Systems
 | GSM | IS-136 | IS-95
Year Introduced | 1990 | 1991 | 1993
Access Method | TDMA | TDMA | CDMA
Base station band | 935–960MHz | 869–894MHz | 869–894MHz
Mobile station band | 890–915MHz | 824-849MHz | 824-849MHz
Channel bandwidth | 200KHz | 30KHz | 1250KHz
Number of channel | 125 | 832 | 20
Users per channel | 8 | 3 | 35
Modulation | GMSK | DQPSK | QPSK

## Slide 22
GSM Enabled Technologies

## Slide 23
Mobile Wireless Data Networks
Driver for Growth
  Popularity of internet
  Desire for anytime, anywhere data communication
Short Message Service (SMS)
Multimedia Messaging Service (MMS)
General Packet Radio Service (GPRS)
Enhanced Data Rates for GSM Evolution (EDGE)

## Slide 24
Constraints with existing network
Data Rates too slow – about 9.6 kbps
Connection setup time too long
Inefficient resource utilization for bursty traffic
Proves expensive for bursty traffic utilization
No efficient method for packet transfers

## Slide 25
Comparison of GSM & GPRS
 | GSM | GPRS
Data Rates | 9.6 Kbps | 14.4 to 115.2 Kbps
Modulation Technique | GMSK | GMSK
Billing | Duration of connection | Amount of data transferred
Type of Connection | Circuit – Switched Technology | Packet - Switched Technology

## Slide 26
Evolution of GSM Networks
© 2011, HTDG,C-DAC

## Slide 27
3G Systems
3G has been in gestation since 1992
International Telecommunications Union (ITU) began
work on a standard called IMT-2000.
IMT stands for International Mobile Telecommunications
The number 2000 initially had three meanings
  The year that services should become available
  The frequency range in MHz that would be used
  and the data rate in Kbits/sec
Regulators, vendors and carriers could not agree
The path to 3G will be gradual, and everyone wants to ensure compatibility with their existing systems

## Slide 28
3G Systems
Voice quality comparable to public switched
telephone network
144kbps data rate for users in high speed vehicles
384kbps to stationary or slow moving users
Support for 2.048 Mbps for office use
Symmetrical and asymmetrical data transmission
rates
Support for both packet and circuit switched data services
More efficient use of spectrum

## Slide 29: 4G (LTE)
LTE stands for Long Term Evolution
Next Generation mobile broadband technology
Promises data transfer rates of 100 Mbps
Based on UMTS 3G technology
Optimized for All-IP traffic

## Slide 30
Thank You
491