## Slide 1: NETWORKING BASICS
BY – ABU TURAB KAZMI

## Slide 2: We will discuss about
OSI Model
TCP/IP Protocol
UDP Protocol
Wi-Fi Standards
WLAN Components

## Slide 3: OSI Model
OSI stands for Open Systems Interconnection. It has been developed by ISO – ‘International Organization for Standardization, in the year 1984. It is a 7-layer architecture with each layer having specific functionality to perform. All these 7 layers work collaboratively to transmit the data from one person to another across the globe.

## Slide 4: Layers of OSI Model

## Slide 5: Physical Layer (Layer 1)
The physical layer contains information in the form of bits.
The functions of the physical layer are as follows:
Bit synchronization
Bit rate control
Physical topologies
Transmission mode

## Slide 6: Data Link Layer (DLL) (Layer 2)
The main function of this layer is to make sure data transfer is error-free from one node to another.
Data Link Layer is divided into two sublayers
  Logical Link Control (LLC)
  Media Access Control (MAC)
  DLL also encapsulates Sender and Receiver’s MAC address in the header.

## Slide 7: Functions of the Data Link layer
Framing
Physical Addressing
Error Control
Flow Control
Access Control

## Slide 8: Network Layer (Layer 3)
The network layer works for the transmission of data from one host to the other located in different networks.
The functions of the Network layer are
  Routing
  Logical Addressing

## Slide 9: Transport Layer (Layer 4)
The transport layer provides services to the application layer and takes services from the network layer.
The functions of the transport layer are as follows
  Segmentation and Reassembly
  Service Point Addressing

## Slide 10: Session Layer (Layer 5)
This layer is responsible for the establishment of connection, maintenance of sessions, and authentication, and also ensures security.
The functions of the session layer are
  Session establishment, maintenance, and termination
  Synchronization
  Dialog Controller

## Slide 11: Presentation Layer (Layer 6)
The data from the application layer is extracted here and manipulated as per the required format to transmit over the network.
The functions of the presentation layer are
  Translation
  Encryption/ Decryption
  Compression

## Slide 12: Application Layer (Layer 7)
This layer serves as a window for the application services to access the network and for displaying the received information to the user.
The functions of the Application layer are
  Network Virtual Terminal
  FTAM-File transfer access and management
  Mail Services
  Directory Services

## Slide 13: TCP/IP Model

## Slide 14: TCP/IP Model
TCP/IP model, was designed and developed by the Department of Defense (DoD) in the 1960s and is based on standard protocols.
It contains four layers
  Process/Application Layer
  Host-to-Host/Transport Layer
  Internet Layer
  Network Access/Link Layer

## Slide 15: The diagrammatic comparison of the TCP/IP and OSI model

## Slide 16: Network Access Layer
This layer corresponds to the combination of the Data Link Layer and the Physical Layer of the OSI model.
It looks out for hardware addressing and the protocols present in this layer allow for the physical transmission of data.

## Slide 17: Internet Layer
This layer parallels the functions of OSI’s Network layer.
The main protocols residing at this layer are
  IP
  ICMP
  ARP

## Slide 18: Host-to-Host Layer or Transport Layer
It is responsible for end-to-end communication and error-free delivery of data. It shields the upper-layer applications from the complexities of data.
The two main protocols present in this layer are
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)

## Slide 19: Application Layer
This layer performs the functions of the top three layers of the OSI model.
Some of the protocols present in this layer are: HTTP, HTTPS, FTP, TFTP, Telnet, SSH, SMTP, SNMP, etc.

## Slide 20: User Datagram Protocol (UDP)
User Datagram Protocol (UDP) is a Transport Layer protocol. UDP is a part of the Internet Protocol suite, referred to as UDP/IP suite. Unlike TCP, it is an unreliable and connectionless protocol.
User Datagram Protocol (UDP) is more efficient in terms of both latency and bandwidth.

## Slide 21: UDP Header

## Slide 22
Source Port: Source Port is a 2 Byte long field used to identify the port number of the source.
Destination Port: It is a 2 Byte long field, used to identify the port of the destined packet.
Length: Length is the length of UDP including the header and the data. It is a 16-bits field.
Checksum: Checksum is 2 Bytes long field.

## Slide 23: Applications of UDP
NTP (Network Time Protocol)
DNS (Domain Name Service)
BOOTP, DHCP.
NNP (Network News Protocol)
Quote of the day protocol
TFTP, RTSP, RIP.

## Slide 24: Thank You